## Slide 1: Astronomy Equipment Basics
Mike Swanson
November 2003
Notes: Astronomy is arguably humankind's oldest science. Historic and prehistoric accounts show that as long as humans have been recording things important to them, the sky has figured prominently. While we have been able to very accurately determine the motion of the objects in the sky for more than three thousand years, it is only a relatively recent development that we have come to understand why they move the way they do. Unfortunately, most folks still don't know the why and most don't even notice the motion!

## Slide 2: Basic Equipment
Binoculars
Best tool for beginners
Both eyes and right side up
Wide field of view
Low magnification
Relatively inexpensive
Telescopes
More stable views
Adjustable magnification
Narrow field of view
Larger aperture
Wide range of costs
Notes: Binos - additional notes:
Specs like 7 x 50 - mag 7, aperture of 50mm
Binos with prices as low at $50 can show amazing views as compared to naked eye
As with all lens, anti-reflective coats improve light transmission – multi-coating best, fully multi-coated indicating all air to glass surfaces.
Use reclining or with bino mounted on tripod (requires bino with tripod mount capability)
Telescopes - additional notes:
Amateur scope costs from less than $100 up to 10s of thousands
Beware of any scopes available in department or “science” stores
If it doesn’t cost at least $200, it will probably be more trouble than it’s worth

## Slide 3: Telescopes
Main function of a telescope is to gather light to a single point, which can then be magnified
Light gathering ability: aperture affects brightness of images and the faintest objects you can see
Light is gathered by the objective - usually a lens or concave mirror
Compare aperture by comparing the area of the objective ( r2 )
The length from the objective to the focus point is called the focal length
Calculate magnification: divide the objective’s focal length by the focal length of the eyepiece in use
Usable magnification is generally about 2 times the diameter of the objective as measured in mm or 50 times the measurement in inches
Finder scope is a smaller scope mounted on the main tube to help you aim at objects in the sky

## Slide 4: Basic Telescope Designs
Refractor
Uses a lens to gather the light to a point
Most rugged design - easy to care for
Gives the sharpest views - especially of planets and the moon
Most expensive for any given aperture
Usually the tube is quite long, although short tube designs are now available
Inexpensive models suffer from chromatic aberration – achromatic vs. apochromatic

## Slide 5: Basic Telescope Designs
Reflector
Uses a mirror to gather the light to a point
Open tube collects dust, mirror eventually tarnishes
Requires periodic alignment (collimating) of the mirrors
Least expensive for any given aperture
Available in both long and short tube design
Generally no chromatic aberration
Most “bang for the buck”

## Slide 6: Basic Telescope Designs
Compound Schmidt-Cassegrain, Maksutov
Uses mirror and lens to gather the light to a point
Sharp views, Maksutov are almost as good as refractors
Closed tube protects optics
Moderate cost for any given aperture
Tube is shortest for any given aperture
Most portable for any given aperture

## Slide 7: Telescope Mounts
Altitude-Azimuth (Alt-Az)
Simple, easy to use
Inexpensive
Most portable
Equatorial
Easy to keep objects in the field of view
More difficult to setup
Usually heavy
Dobsonian (Dob)
Very easy to use
Least expensive
Very stable
Most important: Stability!
Many mounts are motorized, some are computerized!

## Slide 8: Eyepieces and Accessories
Eyepieces - many designs, some costing hundreds of dollars!
Barlow lens - increases magnification from 2x to 3x
Colored filters - for enhanced views of the planets and moon
Light pollution filters - make some nebulae more distinct
Red light flashlight - preserves night vision
Planisphere /Atlas - helps you to find your way around the sky

## Slide 9: Resources
Magazines
Sky and Telescope
Astronomy
Introductory Books
Exploring the Night Sky, Terence Dickinson (kids)
Nightwatch, 3rd Ed., Terence Dickinson
Turn Left at Orion, 3rd Ed., Consolmagno & Davis
The Binocular Stargazer, Leslie Peltier
The Night Sky, David Chandler
Exploring the Night Sky with Binoculars, David Chandler
Intermediate Books
The Backyard Astronomer’s Guide, 2nd Ed., Terence Dickinson
Astronomy: A Self-Teaching Guide, 5th Ed., Dinah Moche
Many of these books are found in the library, all can be purchased at www.skypub.com
Computer Software
TheSky
Starry Night Backyard/Pro
SkyMap Pro
DeepSky2000
Astronomy Clubs
Meetings, Star Parties
Large, club-owned scopes

## Slide 10: Resources
Internet - General Astronomy
SkyMaps.com
www.SkyPub.com
www.Astronomy.com
www.corvus.com -American Association of Amateur Astronomers
www.astroleague.org - Astronomical League
www.EarthSky.com - Earth and Sky
www.nasa.gov - NASA Main Site
nix.nasa.gov - NASA Image Exchange
www.ScopeReviews.com
Internet - Online Stores
www.telescope.com - Orion Telescope
www.Astronomics.com
www.Adorama.com
www.OceansidePhotoAndTelescope.com
www.HandsOnOptics.com
www.Shutan.com
Internet - Telescope Makers
www.Celestron.com
www.Meade.com
www.TeleVue.com
www.telescope.com - Orion Telescope

## Slide 11: Clear Skies!